## Slide 1: Fast Neutron Reactors
A look at the History and current research of Fast Reactor Design
Kevin Fischer || Alex Hagen || Neal Kostry

## Slide 2: Introduction
- Introduction to Fast Neutron Reactors
- History of Fast Neutron Reactors
- Technical Specifications
- Applications and Future Uses

## Slide 3: Fast Neutron Reactors
What is the purpose of a fast neutron reactor?
Fast Neutron Reactors are designed to improve the performance of conventional reactors by utilizing only fast neutrons as a means of initiating fission.
What is the basic concept of operation?
Fast Neutron Reactors utilize uranium much more efficiently due to the production of fissile plutonium isotopes. This allows for the possibility to produce more fuel than is consumed, allowing for fuel “breeding”.

## Slide 4: History of Fast Reactors

## Slide 5: Overview
Fast Neutron Reactors began operation in the early 1950s, and have been operating ever since.
There are over 20 Fast Neutron Reactors worldwide.
There are over 400 reactor years worth of operator experience using Fast Neutron Reactors.
- General purpose of fast reactors are experimental, demonstrational or commercial.

## Slide 6: First EVER FAST Reactor (EBR-1)
EBR-1 (Experimental Breeder Reactor) was the first ever reactor to harvest energy from a nuclear reaction, located at Idaho National Lab.
In December of 1951, EBR-I produced enough electricity to power four 200 watt light bulbs.

## Slide 7: Other Fast Reactors in USA
EBR-II – demonstration reactor run from 1963-1964 to show that a fast reactor can act as a fast or breeder reactor.
Fermi-I – first commercial fast neutron reactor. Located in Michigan and supplied only 66 MWe. Shutdown after only three years due to overheating.
- FFTF (Fast Flux Test Facility) – largest fast reactor in the United States and used for research. Located in Hanford, WA and supplied 400 MWe before shutting down in 1993.

## Slide 8: Fast Reactors Worldwide
- Fast neutron reactors have operated in many countries worldwide, including the United Kingdom, France, Germany, India, Japan, Kazakhstan, Russia, and China.
Some of the more famous of these reactors include the Superphenix in France and the BN-600 in Russia.
  The Superphenix was built to be the largest fast reactor in the world, supplying 1250 MWe. However, the reactor was shut down for political reasons in 1998.
  BN-600 is a fast breeder reactor that is considered to be the most successful reactor built in Russia. It has supplied a constant supply of 600 MWe since 1980.

## Slide 9: Fast Reactors Worldwide (Cont.)
Superphenix (France)
BN-600 (Russia)

## Slide 10: Technical Specifications

## Slide 11: Fuel Design and Moderator
Spectra causes need for different fuel, coolant, building materials
  Few Thermal Neutrons
  No Moderation Needed
  Resonances in Fast region Important
Fast Neutrons causes need for geometric change
  Fast neutrons have longer range
  Leakage will be higher
  Leakage > Res Absorption
Causes large design shift away from moderation

## Slide 12: Reactor Design (Research)

## Slide 13: Reactor Design (Power)

## Slide 14: Reactor Design (Power)

## Slide 15: Optimization Considerations
Little to No Moderation
  Slowing Down Power ~1% of LWR Slowing Down Power
  Sodium Coolant used despite physical difficulties for less moderation
  Oxide fuels provide moderation even though better thermal properties
Resonance Absorptions within non-fissile materials
  Pu vs. U Fuels (ZPPR21)
Reflectors
  Borated Shield, Outer Blanket, (Depleted U) Reflector

## Slide 16: Power Profiles (No Control Rods)
Cosine (at criticality) function within core
Immediate dropoff at borated shield
Fast decrease through blanket
Increase at reflector, same rate decrease,
Dropoff to zero during gap region, protection of operating facility
NO CONTROL RODS IN MODEL

## Slide 17: Power Profiles (Power Reactor)

## Slide 18: Power Profiles (3-D Research)
3-D Cutaway of ZPR6-7 Reactor
Gap Material (Blue) has been removed from top half
Cutaway into core shows color map of power distribution in 3 dimensions
Fission chamber in center (shows low power in chamber)
NO CONTROL RODS IN MODEL

## Slide 19: Applications and Designs

## Slide 20: Fast Reactor Benefits
Fuel Utilization
Hydrogen Production
Desalination
Thermal Efficiency
Passive Safety Systems

## Slide 21: Fuel Benefits
Current Fuel Cycles are Open-Type
  “Once Through” Cycles
  Spent Fuel is left Unused
  High Actinide Production Leads to long lived “hot” waste
  Even with MOX Fuels, Still long term waste problems
  Fuel Repositories are reaching their limits
Fast Reactors to use Thermal Reactor Spent Fuel
  Burn Produced Actinides
  Reduce Proliferation threat – closed fuel cycle burns Pu
  Significantly Reduce wasted fuel

## Slide 22: Fuel Benefits (cont’d)
From Dec. 2005 SciAm - Smarter Use of Nuclear Waste

## Slide 23: Desalination and Hydrogen Production
Desalination
  Location of Plants
  Relatively low temperatures needed
Hydrogen Production
  More economically feasible as temperature increases
  Technologies on Fuel Cells and Electrolysis (Hydrogen Economy)

## Slide 24: Proposed Reactors
Sodium Cooled Fast Reactor
  Designed to burn high level waste from LWR’s
  Operates around 550 °C
  Uses 2 Loops of Liquid Sodium as Coolant
Advantages
  Low Pressure Reactor
  Closed Fuel cycle
  3 different power designs
  Prototypes have been built

## Slide 25: Proposed Reactors (cont’D)
Lead Cooled Fast Reactor
  Very long operating cycles (~20 years)
  Removable core
  Nitride or Metallic Fuel
Advantages
  High Operating Efficiencies
  Negative reactivity feedback
  Low Pressure and Non-reactive with air
  Retains fission products well

## Slide 26: Proposed Reactors (cont’D)
Gas Cooled Fast Reactor
  Helium Cooled Core with Direct Brayton
  Operating Temperature at 850 deg C
  Fuel either Composite Ceramic or new advanced design
  Assemblies are plate or prismatic in design
Advantages
  Easier Hydrogen production
  Very High Efficiencies

## Slide 27: Limitations and Future Research
Sodium Cooled Fast Reactor
  Sodium-Water Interactions and Safety Analysis
Lead Cooled Fast Reactor
  Corrosion in Lead can cause equipment malfunction
  Current Temperature limit is around 450 deg C
Gas Cooled Fast Reactor
  Materials Issues at 850 deg C
  Low heat transfer coefficient
  Safety Concerns for rapid depressurization

## Slide 28: Questions?

## Slide 29: References
Works Cited
Cinotti L., et al., “The ELSY Project”, Paper 377, Proceeding of the International Conference on the Physics of Reactors (PHYSOR), Interlaken, Switzerland, 14-19 September, 2008.
Department of Energy. (2004). Nuclear Hydrogen R&D Plan. District of Columbia: United States Department of Energy.
Generation IV International Forum. (2007). The Sodium-Cooled Fast Reactor. Retrieved November 10, 2011, from Generation IV Technology: http://www.gen-4.org/Technology/systems/sfr.htm
Hannum, W. H., Marsh, G. E., & Stanford, G. S. (2005, December). Smarter Use of Nuclear Waste. Scientific American .
Hill, D. (2006). Global Nuclear Energy Partnership Technology Demonstration Program. Nuclear Physics Conference (pp. 1-14). Idaho National Lab.
Hill, R. N. (2007). NRC Topical Seminar on Sodium Fast Reactors. Fast Reactor Physics. Two White Flint: Argonne National Lab.
US Department of Energy. (2010, December). Generation IV Nuclear Reactors. Retrieved 10 25, 2011, from World Nuclear Organization: http://world-nuclear.org/info/inf77.html